## Slide 1: Modern Operating Systems
Fourth Edition
Chapter 5
Input /Output
Copyright © 2014 Pearson Education, Inc. All Rights Reserved
Notes: If this PowerPoint presentation contains mathematical equations, you may need to check that your computer has the following installed:
1) MathType Plugin
2) Math Player (free versions available)
3) NVDA Reader (free versions available)

## Slide 2: I/O Devices (1 of 2)
Block devices
  Stores information in fixed-size blocks
  Transfers are in units of entire blocks
Character devices
  Delivers or accepts stream of characters, without regard to block structure
  Not addressable, does not have any seek operation

## Slide 3: I/O Devices (2 of 2)
Some typical device, network, and bus data rates.
Device | Data rate
Keyboard | 10 bytes/sec
Mouse | 100 bytes/sec
56K modem | 7 K B/sec
Scanner at 300 dpi | 1 M B/sec
Digital camcorder | 9.5 M B/sec
4x Blu-ray disc | 18 M B/sec
802.1 In Wireless | 37.5 M B/sec
U S B 2.0 | 60 M B/sec
FireWire 800 | 100 M B/sec
Gigabit Ethernet | 125 M B/sec
S A T A 3 disk drive | 600 M B/sec
U S B 9.0 | 625 M B/sec
S C S I Ultra 5 bus | 640 M B/sec
Single-lane P C I e 3.0 bus | 985 M B/sec
Thunderbolt 2 bus | 2.5 G B/sec
S O N E T O C-768 network | 5 G B/sec

## Slide 4: Memory-Mapped I/O (1 of 2)
Figure 5-2. (a) Separate I/O and memory space. (b) Memory-mapped I/O. (c) Hybrid.

## Slide 5: Memory-Mapped I/O (2 of 2)
Figure 5-3. (a) A single-bus architecture. (b) A dual-bus memory architecture.

## Slide 6: Direct Memory Access
Figure 5-4. Operation of a D M A transfer.

## Slide 7: Interrupts Revisited
Figure 5-5. How an interrupt happens. The connections between the devices and the interrupt controller actually use interrupt lines on the bus rather than dedicated wires.

## Slide 8: Precise Interrupt
Four properties of a precise interrupt:
  The P C saved in a known place.
  All instructions before that pointed to by P C have fully executed.
  No instruction beyond that pointed to by P C has been executed.
  Execution state of instruction pointed to by P C is known.

## Slide 9: Precise vs. Imprecise
Figure 5-6. (a) A precise interrupt. (b) An imprecise interrupt.

## Slide 10: Goals of the I/O Software
Issues:
Device independence
Uniform naming
Error handling
Synchronous versus asynchronous
Buffering.

## Slide 11: Programmed I/O (1 of 2)
Figure 5-7. Steps in printing a string.

## Slide 12: Programmed I/O (2 of 2)
Figure 5-8. Writing a string to the printer using programmed I/O.

## Slide 13: Interrupt-Driven I/O
Figure 5-9. Writing a string to the printer using interrupt-driven I/O. (a) Code executed at the time the print system call is made. (b) Interrupt service procedure for the printer.

## Slide 14: I/O Using D M A
Figure 5-10. Printing a string using D M A. (a) Code executed when the print system call is made. (b) Interrupt service procedure.

## Slide 15: I/O Software Layers
Figure 5-11. Layers of the I/O software system.

## Slide 16: Interrupt Handlers (1 of 2)
Typical steps after hardware interrupt completes:
  Save registers (including the P S W) not already saved by interrupt hardware.
  Set up context for interrupt service procedure.
  Set up a stack for the interrupt service procedure.
  Acknowledge interrupt controller. If no centralized interrupt controller, reenable interrupts.
  Copy registers from where saved to process table.

## Slide 17: Interrupt Handlers (2 of 2)
Typical steps after hardware interrupt completes:
  Run interrupt service procedure. Extract information from interrupting device controller’s registers.
  Choose which process to run next.
  Set up the M M U context for process to run next.
  Load new process’ registers, including its P S W.
  Start running the new process.

## Slide 18: Device Drivers
Figure 5-12. Logical positioning of device drivers. In reality all communication between drivers and device controllers goes over the bus.

## Slide 19: Device-Independent I/O Software
A typical page table entry.
Uniform interfacing for device drivers
Buffering
Error reporting
Allocating and releasing dedicated devices
Providing a device-independent block size

## Slide 20: Uniform Interfacing for Device Drivers
Figure 5-14. (a) Without a standard driver interface. (b) With a standard driver interface.

## Slide 21: Buffering (1 of 2)
Figure 5-15. (a) Unbuffered input. (b) Buffering in user space. (c) Buffering in the kernel followed by copying to user space. (d) Double buffering in the kernel.

## Slide 22: Buffering (2 of 2)
Figure 5-16. Networking may involve many copies of a packet.

## Slide 23: User-Space I/O Software
Figure 5-17. Layers of the I/O system and the main functions of each layer.

## Slide 24: Magnetic Disks (1 of 2)
Disk parameters for the original I B M PC 360-KB floppy disk and a Western Digital W D 3000 H L F S (‘‘Velociraptor’’) hard disk.
Parameter | I B M 360-K B floppy disk | W D 3000 H L F S hard disk
Number of cylinders | 40 | 36481
Tracks per cylinder | 2 | 255
Sectors per track | 9 | 63 (avg)
Sectors per disk | 720 | 586,072,368
Bytes per sector | 512 | 512
Disk capacity | 360 K B | 300 G B
Seek time (adjacent cylinders) | 6 msec | 0.7 msec
Seek time (average case) | 77 msec | 4.2 msec
Rotation time | 200 msec | 6 msec
Time to transfer 1 sector | 22 msec | 1.4 usec

## Slide 25: Magnetic Disks (2 of 2)
Figure 5-19. (a) Physical geometry of a disk with two zones. (b) A possible virtual geometry for this disk.

## Slide 26: R A I D (1 of 2)
Figure 5-20. R A I D levels 0 through 3. Backup and parity drives are shown shaded.

## Slide 27: R A I D (2 of 2)
Figure 5-20. R A I D levels 4 through 6. Backup and parity drives are shown shaded.

## Slide 28: Disk Formatting (1 of 3)
A disk sector.
Preamble | Data | E C C

## Slide 29: Disk Formatting (2 of 3)
Figure 5-22. An illustration of cylinder skew.

## Slide 30: Disk Formatting (3 of 3)
Figure 5-23. (a) No interleaving. (b) Single interleaving. (c) Double interleaving.

## Slide 31: Disk Arm Scheduling Algorithms (1 of 3)
Factors of a disk block read/write:
  Seek time (the time to move the arm to the proper cylinder).
  Rotational delay (how long for the proper sector to come under the head).
  Actual data transfer time.

## Slide 32: Disk Arm Scheduling Algorithms (2 of 3)
Figure 5-24. Shortest Seek First (S S F) disk scheduling algorithm.

## Slide 33: Disk Arm Scheduling Algorithms (3 of 3)
Figure 5-25. The elevator algorithm for scheduling disk requests.

## Slide 34: Error Handling
Figure 5-26. (a) A disk track with a bad sector. (b) Substituting a spare for the bad sector. (c) Shifting all the sectors to bypass the bad one.

## Slide 35: Stable Storage (1 of 2)
Uses pair of identical disks
Either can be read to get same results
Operations defined to accomplish this:
  Stable Writes
  Stable Reads
  Crash recovery

## Slide 36: Stable Storage (2 of 2)
Figure 5-27. Analysis of the influence of crashes on stable writes.

## Slide 37: Clock Hardware
Figure 5-28. A programmable clock.

## Slide 38: Clock Software (1 of 3)
Typical duties of a clock driver:
  Maintaining the time of day.
  Preventing processes from running longer than allowed.
  Accounting for C P U usage.
  Handling alarm system call from user processes.
  Providing watchdog timers for parts of system itself.
  Profiling, monitoring, statistics gathering.

## Slide 39: Clock Software (2 of 3)
Figure 5-29. Three ways to maintain the time of day.

## Slide 40: Clock Software (3 of 3)
Figure 5-30. Simulating multiple timers with a single clock.

## Slide 41: Soft Timers
Soft timers stand or fall with the rate at which kernel entries are made for other reasons. These reasons include:
  System calls.
  T L B misses.
  Page faults.
  I/O interrupts.
  The C P U going idle.

## Slide 42: Keyboard Software
Characters that are handled specially in canonical mode.
Character | POSIX name | Comment
CTRL-H | ERASE | Backspace one character
CTRL-U | KILL | Erase entire line being typed
CTRL-V | LNEXT | Interpret next character literally
CTRL-S | STOP | Stop output
CTRL-Q | START | Start output
DEL | INTR | Interrupt process
CTRL-\ | QUIT | Force core dump
CTRL-D | E O F | End of file
CTRL-M | CR | Carriage return (unchangeable)
CTRL-J | NL | Linefeed (unchangeable)

## Slide 43: Output Software – Text Windows (1 of 2)
The ANSI escape sequences accepted by the terminal driver on output. E S C denotes the A S C I I escape character (0x1B), and n, m, and s are optional numeric parameters.
Escape Sequence | Meaning
ESC [n A | Move up n lines
ESC [n B | Move down n lines
ESC [n C | Move right n spaces
ESC [n D | Move left n spaces
ESC [m ; nH | Move cursor to (m,n)
ESC [s J | Clear screen from cursor (0 to end, 1 1from start, 2 all)
ESC [s K | Clear line from cursor (0 to end, 1 1from start, 2 all)

## Slide 44: Output Software – Text Windows (2 of 2)
The ANSI escape sequences accepted by the terminal driver on output. E S C denotes the A S C I I escape character (0x1B), and n, m, and s are optional numeric parameters.
Escape Sequence | Meaning
ESC [n L | Insert n lines at cursor
ESC [n M | Delete n lines at cursor
ESC [n P | Delete n chars at cursor
ESC [n @ | Insert n chars at cursor
ESC [n m | Enable rendition n (0=normal, 4=bold, 5=blinking, 7=reverse)
ESC M | Scroll the screen backward if the cursor is on the top line

## Slide 45: The X Window System (1 of 4)
Figure 5-33. Clients and servers in the M.I.T. X Window System.

## Slide 46: The X Window System (2 of 4)
Types of messages between client and server:
  Drawing commands from program to workstation.
  Replies by workstation to program queries.
  Keyboard, mouse, and other event announcements.
  Error messages.

## Slide 47: The X Window System (3 of 4)
Figure 5-34. A skeleton of an X Window application program.

## Slide 48: The X Window System (4 of 4)
Figure 5-34. A skeleton of an X Window application program.

## Slide 49: Graphical User Interfaces (1 of 4)
Figure 5-35. A sample window located at (200, 100) on an X G A display.

## Slide 50: Graphical User Interfaces (2 of 4)
Figure 5-36. A skeleton of a Windows main program.

## Slide 51: Graphical User Interfaces (3 of 4)
Figure 5-36. A skeleton of a Windows main program.

## Slide 52: Graphical User Interfaces (4 of 4)
Figure 5-37. An example rectangle drawn using Rectangle. Each box represents one pixel.

## Slide 53: Bitmaps
Figure 5-38. Copying bitmaps using BitBlt. (a) Before. (b) After.

## Slide 54: Fonts
Figure 5-39. Some examples of character outlines at different point sizes.

## Slide 55: Hardware Issues
Power consumption of various parts of a notebook computer.
Device | Li et al. (1994) | Lorch and Smith (1998)
Display | 68% | 39%
C P U | 12% | 18%
Hard Disk | 20% | 12%
Modem | Blank | 6%
Sound | Blank | 2%
Memory | 0.5% | 1%
Other | Blank | 22%

## Slide 56: Operating System Issues: The Display
Figure 5-41. The use of zones for backlighting the display. (a) When window 2 is selected it is not moved. (b) When window 1 is selected, it moves to reduce the number of zones illuminated.

## Slide 57: Operating System Issues: The C P U
Figure 5-42. (a) Running at full clock speed. (b) Cutting voltage by two cuts clock speed by two and power consumption by four

## Slide 58: Copyright